ECE347

Lab2

(Amplifier Frequency Rersponse)

Introduction:

The objective is to obtain the common emitter amplifier frequency response, draw the bode plots.

Procedure:

Implement the following common emmiter amplifier. Use a voltage divider in the front to get the small signal. Then, measure the gain (Vout/Vin) for the frequencies in the table.

| Frequency (Hz) | Gain (Vout/Vin) |
| --- | --- |
| 5 |  |
| 10 |  |
| 20 |  |
| 50 |  |
| 100 |  |
| 1k |  |
| 10k |  |
| 20k |  |
| 30k |  |
| 40k |  |
| 50k |  |
| 100k |  |
| 200k |  |

From your measurements, find the -3dB frequencies, and draw the bode plot for the amplitude gain only.

2. Sqaure Wave Technique to determine the frequency response of a circuit : Now apply a square wave signal of T=10 Hz and amplitude of 4 V to the input of the circuit and observe the output signal on the oscilloscope.

This time obtain the upper and lower cut-off frwquencies of the circuit by using the formulas

fH=0.35/tR, where tR is the rise time of the signal,

fL=P.fS/(, where P=V-V’/V, where P is called thetilt of the signal.

Note these formulas and its proper applications are given in your text book pp. 583-586.

Questions:

- Compare the cut-off frequencies obtained in the two methods for the circuit and comment about the result.

- Why there is arise time and tilt problem when we apply a square wave?  Explain this by using Fourier Transforms and frequency domain behaviour of the circuit.

- How do you think that phase shift caused by the circuit will change by frequency? Explain.